## Slide 1: 微机原理上机实验
2017.11.8

## Slide 2: 编程、调试工具
汇编：MASM或者TASM
链接：LINK或者TLINK
调试：DEBUG或TD

## Slide 3: 汇编语言程序开发步骤
编辑源程序
  文本文件: *.asm
汇编源程序
  形成目标文件: *.obj
连接目标文件
  输出可执行文件: *.exe
调试可执行文件
Edit (notepad, ultraedit, …)
Assemble (masm, tasm, …)
Link (link, tlink, …)
Debug (debug, td, …)
*.asm
*.obj
*.exe
出
错
Notes: Masm 6.11

## Slide 4: 示例－汇编语言源程序
// C Program “Hello.c”
#include <stdio.h>
void main ( )
{
printf (“Hello, World!\n” );
}
; 8086 Assembly Program “Hello.asm”
SSEG SEGMENT ; Stack Segment
DB 256 DUP(?)
SSEG ENDS
DSEG SEGMENT ; Data Segment
HELLO DB 0DH, 0AH, “Hello, World!”, 0DH, 0AH, “$”
DSEG ENDS
CSEG SEGMENT ; Code Segment
ASSUME CS:CSEG, DS:DSEG, SS:SSEG
START: MOV AX, DATA ; 初始化DS
MOV DS, AX
LEA DX, HELLO ; 显示字符串
MOV AH, 09H
INT 21H
MOV AX, 4C00H ; 返回DOS
INT 21H
CODE ENDS
END START

## Slide 5: 终止程序
结束用户程序，返回调用程序或操作系统
常用方法：
(1) 在程序最后，加2条指令
MOV AH，4CH ; AL可放置返回码
INT 21H
(2) 在程序开始，添加下面3条指令
PUSH DS
XOR AX，AX
PUSH AX
在程序最后，放一条RET指令
Notes: RET应是远程返回！否则将出现重复执行主程序，直至堆栈溢出出错而退出。

## Slide 6: 基本输入/输出
键盘输入
  带回显字符输入
  不带回显字符输入
  带回显字符串输入
屏幕输出
  字符输出
  字符串输出

## Slide 7: 键盘输入
带回显的字符输入
  功能：等待从键盘输入一按键，并显示在屏幕上
  入口参数：AH = 1
  出口参数：AL = 按键的ASCII码
不带回显的字符输入
  除AH=8和不显示键入的字符外，其他同上
Notes: function 01h
Filtered input with echo
  This function returns the next character in the keyboard buffer (waiting if necessary)
  The character is echoed to the screen
  AL will contain the ASCII code of the non-control character
    AL=0 if a control character was entered
08h - Direct input with Ctrl-Break
Ctrl-Break will cancel the input request and terminate the program

## Slide 8: 键盘输入(续)
带回显的字符串输入
  功能：等待从键盘输入以回车结束的一串字符，并存入设定的缓冲区，同时显示在屏幕上
  入口参数
    AH = 10, DS : DX = 缓冲区首址, 其中 [DS : DX] = 缓冲区大小 (1~255)，例如： Buf DB 5, ?, 5 dup(?)
  出口参数
    [DS : (DX+1)] = 输入字符数(除回车外), 输入的字符串从DS : (DX+2)开始存放
Notes: 0Ah - Buffered input
A buffer of up to 255 characters is used
Backspace can be used to delete characters
Other control keys are filtered
Characers are echoed
Enter key terminates the input phase
  DX must contain the offset to a buffer area
  buffer db m, ?, m dup (?)
06h : Direct input, no waiting
No filtering
No on-screen echo
  requires DL = 0FFh
  Does not wait for a character to be input
  ZF set if no character is waiting
07h : Direct input, no Ctrl-Break
  Ctrl-Break while waiting for input will not terminate program
0Bh - Get input status
AL is set to 0FFh if a character is waiting in the keyboard buffer, AL = 0 otherwise
The keyboard buffer is a 15-character queue holding keystrokes not yet processed by an application
  DOS manages this via hardware interrupts
  A "beep" indicates the buffer is full
    additional keystrokes are ignored when full
0Ch - Clear input buffer, invoke input function

## Slide 9: 屏幕输出
字符输出
  功能：在屏幕上显示一个字符
  入口参数：AH = 2, DL = 待显示ASCII码字符
  出口参数：无
字符串输出
  功能：在屏幕上显示一个字符串
  入口参数：AH = 9, DS:DX =以’$’结束的ASCII码字符串的起始地址
  出口参数：无
Notes: Interrupt 21h, function 09h
  DX = offset to the string (in data segment)
  The string is terminated with the '$' character

## Slide 10: 练习TD的使用

## Slide 11: 上机练习题
第10～11周
统计寄存器BX（二进制数）中 “1” 的个数。
统计一组数据（字节型有符号数）中正数、负数和零的个数。
将寄存器BX中无/有符号数，以二/十六/十进制格式显示在屏幕上
从键盘输入一个二/十六/十进制数存入BX
从键盘输入一字符串，将所有英文字母变成大写，然后整串以反序输出在屏幕上

## Slide 12: 上机检查题
第12～15周，每周检查一题
把1~36的自然数按行顺序存入一个6*6的二维数组中，然后打印出该数组的左下半三角
编程实现排序算法，对某文件（txt格式）中的无符号整数进行排序，排序结果输出到屏幕（数据的个数不超过1024）
计算N!（0<N<20）
编程计算任一整数加减运算表达式，其中，表达式长度不超过1024个字节，从键盘输入，可带括号，操作数为字数据

## Slide 13: 接口实验与上机考试
第16周
  8255接口实验
第17周
  汇编程序设计上机考试